## Slide 1
SLIIT · IT4010 Research Project · May 2026
Edge-Based Energy-Efficient
IoT Smart Waste Management System
Progress Presentation 1 · 50% Milestone
R26-IT-169 | Perera G.M.T | IT21196638
B.Sc. (Hons) Information Technology · Department of Information Technology
GAP FOCUS
Joint Adaptive
Control Policy
HARDWARE
ESP32 + 4 Sensors
(Working Prototype)
PIPELINE
IoT → MQTT → Edge
→ Live Dashboard

## Slide 2
PROBLEM STATEMENT & RESEARCH GAP
CURRENT IMPLEMENTATIONS FAIL
Existing IoT approach (Thakker & Shaikh 2015; Shyam et al. 2017):
Bin Node → transmit raw sensor data every 60s → Cloud → Dashboard
This creates three unsolved problems:
Battery drain — Wi-Fi TX draws 240mA peak; fixed 60s rate = ~62 day battery on 2000mAh
Bandwidth waste — stable bin at 30% fill still transmits 60×/hr; 95% of TXs carry no actionable data
No adaptive intelligence — existing systems (Longhi 2012; Sankeerth 2020) don't adjust based on battery, fill velocity, or channel quality
RESEARCH GAP (GAP 1)
Closest prior art — Giordano et al. (ENSsys'23):
FSM + AIMD adapts sampling rate only (one output)
No deadband, urgency override, AoI floor, or bin context
Our contribution — joint 4-output policy on one node:
T*
TX interval — AIMD on battery SoC
ΔF*
Deadband — fill velocity adaptive
U
Urgency — fill + gas + rate signal
AoI
Max suppression floor per FSM state

## Slide 3
HIGH-LEVEL SYSTEM ARCHITECTURE
Smart Bin Node
ESP32 + Sensors
▸ HC-SR04 fill level
▸ MQ-135 / MQ-5 gas
▸ DHT22 temp/humidity
▸ Battery monitoring
MQTT
Edge Gateway
Laptop (PP1) / Pi (PP2)
▸ Rule-based filtering
▸ AIMD + deadband FSM
▸ Cluster arbitration
▸ Adaptive TX control
REST/WS
Cloud Backend
Node.js + SQLite
▸ REST API
▸ Socket.io fanout
▸ Event storage
▸ Authentication
WebSocket
Web Dashboard
React + Vite
▸ Live FSM state
▸ TX comparison
▸ Gas/fill charts
▸ Battery control
Mobile App
React Native Expo
▸ Collection alerts
▸ Issue reporting
▸ Schedule view
▸ (PP2 milestone)
PP1 scope: Smart Bin Node + Cloud Backend + Web Dashboard live. Edge Gateway (Raspberry Pi) + Mobile App deferred to PP2 per WBS.

## Slide 4
JOINT ADAPTIVE CONTROL POLICY — OVERVIEW (4 OUTPUTS)
ALERT
T* = 30s
ΔF* = 1%
fill ≥ 80% OR gas > threshold OR dF/dt > 10%/hr
ACTIVE
T* = 90s
ΔF* = 3%
fill ≥ 60% OR dF/dt > 2%/hr
STABLE
T* = 300–1800s (AIMD)
ΔF* = 1–10%
Default state — AIMD governs interval from battery SoC
CONSERVE
T* = 600s
ΔF* = 5%
battery < 30% (ALERT urgency override always wins)
AIMD: batt > 80% → T* ÷ 2 | batt < 70% → T* + 60s | 70–80%: hold Deadband: ΔF* = max(1%, 10% − dF/dt × 0.5) AoI floor enforced per state

## Slide 5
OUTPUT 1: T* — TRANSMISSION INTERVAL (AIMD Control Law)
What it is
T* is how long the ESP32 waits before the next transmission. It adapts based on battery level using AIMD — the same control law TCP uses for congestion. Battery = congestion signal: batt > 80% → halve T* (send more, you have power) batt < 70% → add 60s (send less, conserve) 70–80% → hold (hysteresis, stop thrashing)
Walk-through example
Start:
T* = 300s, battery = 90%
90% > 80%:
300 × 0.5 = 150 → floored to 300s
battery → 65%:
300 + 60 = 360s
still 65%:
360 + 60 = 420s (climbing toward 1800s cap)
battery → 85%:
420 × 0.5 = 210 → floored to 300s
In config.h
firmware/include/config.h
#define AIMD_MIN 300000UL // floor: 300s
#define AIMD_MAX 1800000UL // ceiling: 1800s
#define AIMD_AI 60000UL // additive +60s
#define AIMD_MD 0.5f // multiplicative ×0.5
In fsm.h — STABLE branch
firmware/src/fsm.h (STABLE else-branch)
if (ctx.state != State::STABLE)
ctx.txInterval = AIMD_MIN; // reset on re-entry
if (battPct > BATT_AIMD_MD_THRESH) { // >80%
ctx.txInterval *= AIMD_MD; // halve
ctx.txInterval = max(txInterval, AIMD_MIN);
} else if (battPct < BATT_AIMD_AI_THRESH) {//70%
ctx.txInterval = min(txInterval+AIMD_AI, AIMD_MAX);
} // 70–80%: nothing (hysteresis)
In main.cpp — transmission gate:
firmware/src/main.cpp
bool timerFired =
(now - lastTxMs >= fsm.txInterval);

## Slide 6
OUTPUT 2: ΔF* — DYNAMIC DEADBAND (Send-on-Delta, Miskowicz 2006)
What it is
Even when the timer fires, we don't transmit if fill hasn't actually changed enough. ΔF* is the minimum fill change needed to trigger a TX.
When the bin is stable → wide deadband (suppress HC-SR04 noise).
When filling fast → narrow deadband (catch real changes).
Formula: ΔF* = max(1%, 10% − dF/dt × 0.5)
dF/dt
ΔF*
Effect
0 %/hr
10%
Bin stable — suppresses ±1cm sensor noise
4 %/hr
8%
Slow fill — still ignores small fluctuations
10 %/hr
5%
Medium fill — catches most real changes
18 %/hr
1%
Fast fill — transmits on almost every reading
In fsm.h — computeDeadband()
firmware/src/fsm.h
static float computeDeadband(float dFdt) {
// dFdt is in %/s — convert to %/hr first
float dFdt_hr = dFdt * 3600.0f;
float db = 10.0f - dFdt_hr * 0.5f;
return max(1.0f, db); // never fully suppress
}
dF/dt calculation — from fsm.h:
firmware/src/fsm.h (top of fsmUpdate)
uint32_t dt = nowMs - ctx.lastSampleMs;
// fill velocity in %/s
float dFdt = (fillPct - ctx.prevFill) / (dt/1000.0f);
deadbandOut = computeDeadband(dFdt);
Used in main.cpp — transmission gate:
firmware/src/main.cpp
// how much has fill moved since last TX?
float fillDelta = fabs(r.fillPct - lastTxFill);
bool deadbandCrossed = (fillDelta >= deadband);
// TX fires if timer OR deadband OR urgency

## Slide 7
OUTPUT 3: URGENCY OVERRIDE (Priority Always Beats Energy Conservation)
Priority evaluation order — runs every loop tick:
1
Urgency check
fill ≥ 80% OR gas > threshold OR dF/dt > 10%/hr → ALERT
2
Battery check
battery < 30% → CONSERVE (only if urgency false)
3
Activity check
fill ≥ 60% OR dF/dt > 2%/hr → ACTIVE
4
Default
none of above → STABLE (AIMD runs here)
The stateChanged guard — critical detail:
Without stateChanged, every loop tick while fill ≥ 80% would transmit (~55 times/min — worse than baseline).
With stateChanged: urgency fires ONCE on ALERT entry → one immediate TX. After that, the 60s AoI floor (txInterval) controls cadence.
Result: fast alert + controlled energy.
In fsm.h — urgency check (ALWAYS first):
firmware/src/fsm.h (fsmUpdate — priority order)
// 1. URGENCY — runs before battery check
if (fillPct >= FILL_ALERT // ≥80%
|| gasRaw135 > GAS135_THRESHOLD
|| gasRaw5 > GAS5_THRESHOLD
|| (dFdt*3600.0f) > DFDT_ALERT) {//10%/hr
ctx.state = State::ALERT;
ctx.txInterval = AoI_ALERT; urgent = true;
} // battery check comes AFTER — never suppresses alert
In main.cpp — stateChanged gate:
firmware/src/main.cpp (ADAPTIVE branch)
static State prevState = State::STABLE;
bool stateChanged = (fsm.state != prevState);
prevState = fsm.state;
// fire ONCE on entry, not every tick
if ((urgent && stateChanged) ||
timerFired || deadbandCrossed) { publish(); }
Reason strings (visible in dashboard):
firmware/src/main.cpp
reason = fillPct>=FILL_ALERT ? "urgency-fill"
: gasRaw135>THRESH135 ? "urgency-gas135"
: gasRaw5>THRESH5 ? "urgency-gas5" : "urgency-rate";

## Slide 8
OUTPUT 4: AoI FLOOR (Maximum Suppression — Node Can Never Go Silent)
What it is
AoI = Age of Information — how stale is the data at the receiver?
Without an AoI floor, a bin that is 75% full but not changing could go silent indefinitely — deadband never crossed, no urgency. The dashboard would not know if the node is alive or dead.
The AoI floor is a forced heartbeat: transmit at least once every N seconds, regardless of deadband.
AoI floor values per state:
ALERT
60s
Overflow risk — operator MUST have current data
ACTIVE
5 min
Filling trend trackable for overflow prediction
STABLE
30 min
Heartbeat only — confirms node is alive
CONSERVE
15 min
Battery critical — less frequent but never silent
In config.h — AoI constants:
firmware/include/config.h
#define AoI_ALERT 60000UL // 60s
#define AoI_ACTIVE 300000UL // 5min
#define AoI_STABLE 1800000UL // 30min
#define AoI_CONSERVE 900000UL // 15min
In fsm.h — AoI IS the txInterval per state:
firmware/src/fsm.h (state transitions)
if (fill >= FILL_ALERT || gas || rate) {
ctx.txInterval = AoI_ALERT; // 60s floor
} else if (batt <= BATT_LOW) {
ctx.txInterval = AoI_CONSERVE; // 15min floor
} else if (fill >= FILL_ACTIVE) {
ctx.txInterval = AoI_ACTIVE; // 5min floor
} // STABLE: AIMD governs, max = AIMD_MAX = 1800s
In main.cpp — enforced via timer:
firmware/src/main.cpp
// AoI floor = txInterval in non-STABLE states
bool timerFired = (now-lastTxMs >= fsm.txInterval);
AoI insight: In ALERT/ACTIVE/CONSERVE, txInterval IS the AoI floor. In STABLE, AIMD governs txInterval but AIMD_MAX (1800s) acts as the implicit AoI ceiling.

## Slide 9
PROOF OF CONCEPT — CURRENT IMPLEMENTATION
ESP32 Serial Monitor — FSM State Transitions
[WiFi] connecting to Redmi Note 14...
[WiFi] connected, IP=10.97.85.244
[RTC] fresh boot, initializing
[MQTT] connecting... ok
[MQ] warmup complete
[FSM] state=STABLE interval=300s
[TX] {"state":"STABLE","fill":12.4,"reason":"timer"}
[FSM] state=ACTIVE interval=90s
[TX] {"state":"ACTIVE","fill":64.2,"reason":"timer"}
[FSM] state=ALERT interval=60s
[TX] {"state":"ALERT","fill":82.1,"reason":"urgency-fill"}
[FSM] CONSERVE (batt=25%)
MQTT PIPELINE — VERIFIED
ESP32
Sensors read + FSM evaluated every 1s
MQTT
Mosquitto broker @ 10.97.85.244:1883
Node
Ingests + stores 15-field JSON to SQLite
Dash
Socket.io → live update every transmission
bin/bin01/data — Live MQTT Payload
{"node_id":"bin01","mode":"ADAPTIVE",
"state":"STABLE","fill_pct":23.4,
"gas_135":1280,"gas_5":2340,
"batt_pct":80,"temp_c":29.8,
"interval":300,"deadband":9.8,
"dfdt":0.12,"reason":"timer","tx_count":7}
✓ WiFi + MQTT verified ✓ FSM state transitions live ✓ Dashboard real-time ✓ Battery slider controls CONSERVE ✓ 4 sensors operational

## Slide 10
TECHNOLOGY STACK & STANDARDS APPLIED
IoT Firmware Layer
▸ ESP32-D0WD-V3 NodeMCU 38-pin — 240MHz dual-core, RTC memory for FSM state persistence
▸ HC-SR04 fill level (median-of-3 filter) · MQ-135 VOC · MQ-5 LPG/methane · DHT22 temp/humidity
▸ PlatformIO + Arduino framework · PubSubClient (MQTT) · ArduinoJson · Espressif ESP-IDF deep sleep API
Communication & Backend
▸ MQTT protocol (ISO/IEC 20922) via Mosquitto broker — lightweight pub/sub, QoS 0, 200-byte payloads
▸ Node.js + Express RESTful API (REST architectural style, HTTP/1.1) · Socket.io WebSocket fanout
▸ better-sqlite3 — structured event store; 15-field normalised schema per reading
Standards & Best Practices
▸ IEEE citation format — 12 peer-reviewed references (ACM, IEEE IoT Journal, PLOS ONE, ENSsys)
▸ FSM design pattern (Giordano ENSsys'23) · AIMD control law (TCP Reno) · Send-on-delta (Miskowicz 2006)
▸ Code: modular headers (config.h, fsm.h, sensors.h) · inline comments · separation of concerns · version-pinned libs

## Slide 11
REQUIREMENTS · WBS PROGRESS · RISK MITIGATION
ID | Requirement | Status
FR1 | IoT node captures fill, gas, temp, battery | ✓ Done
FR2 | Node sends via MQTT lightweight protocol | ✓ Done
FR3 | Edge gateway aggregates multiple bins | PP2
FR4 | Edge applies rule-based FSM filtering | ✓ Laptop
FR5 | Edge adapts TX using battery + network | ✓ Done
FR6 | Web app displays bin status + trends | ✓ Done
FR7 | Web app supports route-planning | PP2
FR8 | Mobile app — schedules, alerts, reporting | PP2
FR9 | Backend stores data securely | ✓ Done
WBS at 50% milestone:
1-2 Problem+Reqs
100%
3 IoT Prototype
100%
5 Backend+DB
90%
6 Dashboard
85%
4 Edge Gateway
15%
7 Mobile App
10%
RISK MITIGATION
Sensor inaccuracy / MQ drift
Med
Gateway failure
Med
Network instability
Med
Scope creep (mobile/cluster deferred)
Low
Boot-mode conflict (strapping pins)
Low

## Slide 12
COMMERCIALIZATION & NEXT MILESTONE
COMMERCIALIZATION
Target Markets
Municipal councils & private waste firms
Residential complexes, universities, hospitals
Revenue Model
One-time hardware: smart-bin + gateway cluster
Monthly SaaS: dashboard + analytics + support
Managed services + municipal integrations
Value Proposition
~60% TX reduction → lower data costs + longer battery
Edge resilience — works without internet connectivity
PP2 MILESTONE TARGETS
WBS-4
Raspberry Pi edge gateway — rule engine, cluster arbitration, OVERRIDE_T feedback loop
WBS-7
Mobile app — collection schedules, push alerts, issue reporting (React Native)
WBS-8
System integration — 3-node cluster simulation, end-to-end evaluation
WBS-9
Quantitative evaluation — measured TCR, AR, BLEF against fixed-interval baseline
SDG Alignment: SDG 11 (Sustainable Cities) + SDG 12 (Responsible Consumption). Key differentiator: First joint AIMD + deadband + urgency + AoI policy on a single ESP32 node applied to smart waste.